## Slide 1: Chap3: Receiver Firmware Upgrades
Upgrading Receiver Firmware
Notes: From time to time, new firmware revisions come out for the GPS receivers as well. These firmware files are downloadable from the Topcon website. Make sure to get the correct file for the receiver in question.

## Slide 2
Setting Connection Parameters
Notes: The default settings will probably never have to be changed unless the COM1 port on the computer is in use by another piece of hardware. All of the other settings should never have to be changed.

## Slide 3
Query Receiver Information
Step 2
Step 3
Notes: Select the Device tab.
Select Receiver from the Device Type pull-down menu.
Select Get from Device to retrieve the current information on the receiver.

## Slide 4
Download Receiver Firmware
Notes: Match the information from the previous page to the table on the website to find the appropriate firmware file to download.
Once the file has been downloaded, unzip the file.

## Slide 5
Load Receiver Firmware
Step 5
Step 6
Step 7
Step 8
Step 4
Notes: Select the Program tab.
Select Soft Break Capture from the Capture Method pull-down.
Browse for the ramimage.ldr file from the zip file that was downloaded from the internet.
Browse for the main.ldp file from the zip file that was downloaded from the internet.
Select the Load button to load the receiver with the current firmware file settings.
Once the firmware is done loading, the status bar at the bottom of the screen will read 100%.

## Slide 6
Query Power Board Information
Step 9
Step 10
Step 11
Notes: For HiPer and OdysseyE receivers, there is also an internal power board for the receiver. This file is included in the zip file for the appropriate receivers.
Select the Device tab again.
Select Receiver’s Power Board from the Device Type pull-down menu.
Select Get from Device to retrieve current values.
Select the Program tab.

## Slide 7
Load Power Board Firmware
Step 12
Step 13
Notes: Browse for the powbrd.ldr file from the zip file that was downloaded from the internet.
Select the Load button to load the receiver with the current firmware file settings.
Once the firmware is done loading, the status bar at the bottom of the screen will read 100%.

## Slide 8
Incorrect Firmware Load Attempted
Notes: If an incorrect file is selected to be loaded, the Floader program will not allow that to happen. An error message will be displayed.